## Slide 1: Azure IoT Hub Device Management Private Preview
NDA - Microsoft Confidential
Carlos Alayo, Ellen Farber, Juan Perez
Program Management
Azure IoT

## Slide 2: Private Preview Goals
Further understand customer scenarios and needs
Update partners/customers on progress for DM capabilities.
Get feedback on DM APIs (device and service) from developers who have worked with DM in industrial automation and manufacturing.

## Slide 3: Expectations of Customers
8 hour time commitment - extremely light weight
  MS PM onsite visit to ensure high bandwidth conversation and feedback when completing the walkthrough
Complete walkthrough for following scenarios:
  Tags: Add service properties (tags) to managed device and query for all devices with specified tag
  Device Property Sync: Change device property and view the change from service client
  Firmware Update: Complete firmware update workflow on simulated device or Intel Edison

## Slide 4: Agenda
Your world – Introduction
The IoT Solution Discussion
Azure IoT overview (Deck) and sample walkthrough
Dive into the code and understand the Azure IoT Hub DM APIs
Mapping your solution to our capabilities
Wrap up – next steps

## Slide 5: The IoT Solution Discussion
Personas Involved
The Device
Device Health
Device Actions
Organizing Devices
Device State

## Slide 6: Azure IoT Hub Device Management Schedule
Q2 CY 2016
DM Public Preview*
Q3 CY 2016
DM Generally Available**
2016
Q1 CY 2016
DM Private Preview
* DM delivered only in new IoT Hub instances that include DM
** DM available to all new and existing IoT Hubs

## Slide 7: Azure IoT Solution

## Slide 8: The Problem: Why do we need Device Management?
New IoT devices need to be enrolled
Devices need to be maintained through monitoring, access, and updates
  Configuration is the most desirable as it’s the least disruptive
  Firmware and Software as a last resort when firmware/software is not configurable
  Direct access through SSH or RDP when required by configuration
Devices need to be organized into a number of structures
  RBAC hierarchy to enable users to manage subsets of the devices
  Business relationships between devices for a number of reason (discovery, containment, ownership/assignment, impact analysis, audit, integration with 3rd party systems).
Data coming from devices needs to be decorated by DM metadata
Devices ultimately are decommissioned and/or disposed

## Slide 9: Azure IoT Device Management Goals
Helps operators understand device health for millions of devices through device properties.
Helps operators maintain devices through device jobs.
  Example device management jobs:
    Firmware Update
    Configuration Update
    Reset/Reboot
    Factory Reset

## Slide 10: Azure IoT Hub DM Service Client Architecture
Azure IoT Hub
Device Management APIs
Device Query API
Tags, Device and Service Properties
Jobs Client API
Create, Monitor, Cancel
LWM2M
over CoAP/TCP
Device with DM
DM Client Library
Device App
Your Code
Registry Manager API
Create, Update, Delete Devices
Application
Your Code
IoT Cloud Solution
Device Management Objects
Device
(Object)
System Properties
Custom Properties
Service Properties

## Slide 11: Device Representation in IoT Hub Service
Device
.NET Type: Microsoft.Azure.Devices
System Properties
Device is Master
Battery Info
Firmware Version
HW Version
Mfg Name
…
Custom Properties
(Enabled in GA)
Service Properties
Service is Master
Tags
Device Fields
Device Connection Info
Authentication
Connection String
Connection State
Device Status Info
Status
Status Reason
Status Update Time

## Slide 12: Azure IoT Hub DM Device Client Architecture
Device using IoT Hub DM library
IoT Hub DM library
LWM2M
over CoAP/TCP
IoT Hub
Your Code
Invokes callbacks for Read, Write and/or Execute
Implement Callback
Implement Callback
LWM2M Objects
Server Object
LWM2M Server Properties
Config Object
FW Update Object
Download FW, Update FW, Post-update
Device Object
Device Properties, Reboot, Factory Reset
.
.
.

## Slide 13: Device Job (Firmware Update Example)
A Device Job is a multi-step device orchestration on a set of devices managed by Azure IoT Hub.
IoT Hub
Device
Your Code
On the device
IoT Hub DM library
Step 1
Step 2
Step 3
Device Job*
Write FW Package URI
Change the Package URI
Invoke callback for Package URI
Download Completed
Download the Code
Apply the Update
Invoke callback to Apply Update
Reconnect after restart
Monitor State Changes and Apply Update
IoT Cloud Solution
Your Code
In the Service
Step 1: Start Firmware Update Job, providing the Package URI
On Job Completed: Receive callback in service.
Anytime during job execution: Check the status of the Job.
* A job works against a set of devices. Showing only a single device in this diagram.

## Slide 14: Azure IoT DM Public Preview Features Q2 CY 2016
Device Management Client Lib
  Part of IoT Hub SDK
  C and Node.js
  DM Samples
    Intel Edison & Simple API sample
Device Query - Service API
  Tags
  Device Properties
  Service Properties
Device Jobs - Service API
  Create (single or set of devices)
  Start/Stop Jobs
  Inspect Jobs Progress
  Delete Jobs
Device Jobs (instances)
  Firmware Update
  Configuration Update
  Reset/Reboot
  Factory Reset
DM Forwarding to push DM events into IoT Hub Event Hub

## Slide 15: Azure IoT DM GA Features Q3 CY 2016
Device Management Client Lib
  Part of IoT Hub SDK
  C, Node.js and Java
  DM Samples
    Intel Edison & Simple API sample
    More device samples
Device Query - Service API (C#)
  Tags
  Device Properties
  Service Properties
  Topology
Device Jobs - Service API (C#)
  Create (single or set of devices)
  Start/Stop Jobs
  Inspect Jobs Progress
  Delete Jobs
Device Jobs (instances) (C#)
  Firmware Update
  Configuration Update
  Reset/Reboot
  Factory Reset
DM Forwarding to push DM events into IoT Hub Event Hub
Device Topology – Service API
  RBAC (Role based access control) for device groups
Device Models – Service API
  Custom Device Properties
  Map LWM2M objects to Device Properties
Underlined new in GA

## Slide 16: Azure IoT Hub Patterns Working with the existing APIs and DM APIs
Device
IoT Hub
Cloud
Gateway
HTTP
AMQP
MQTT
Event Hub
Device
IoT Hub
Cloud
Gateway
LWM2M over
CoAP/TCP
A = 5, 1:14p 3/3/2015
B = 2, 1:14p 3/3/2015
C = 4, 1:14p 3/3/2015
Device Properties
Device Properties
A = 500000
B = 2
C = 4
Client:
Messaging
Device
Client
Client:
Device
Properties
Client (for
Device)
Last known values
at this time stamp
Client:
Device
Properties
Client (for Service)
Possible Clients:
Azure Stream Analytics
Event Processor Host
Direct Read from IoT Hub
Storm for EH
Messages
Unique to Messaging:
Messages sent by device
Frequency of messages defined by device
Service receives messages in an EventHub
Unique to Device Property Sync:
Properties are set by the device, but not sent to service
Moving the properties from device to service is coordinated by the service
Service reads properties for a specific device
Other devices

## Slide 17: Limitations during Private Preview
Scale to 100 devices per hub
Database may be wiped at any time
Only use for sample code or PoC testing, not for a production environment
DM APIs will change based on feedback from private preview and we will not support back compatibility with the current APIs
Messages sent between IoT hub and device are not encrypted
DM Enabled IoT Hubs will only be available for use during the DM private preview workshop.

## Slide 18: Give us feedback
Contact Us Contact Uss: azureiotdm@microsoft.com

## Slide 19: Appendix

## Slide 20: Current supported resources in Device Object
LWM2M tutorials can be found here and here. LWM2M objects registry is here.
Resource Name | Resource ID | Operation | Type | Range and Units | Description
Manufacturer | 0 | Read | String |  | Manufacturer name
Model Number | 1 | Read | String |  | A model identifier (manufacturer specified string)
Device Type | 17 | Read | String |  | Type of device (manufacturer specified string)
Serial Number | 2 | Read | String |  | Serial number of device
Firmware Version | 3 | Read | String |  | Current firmware version of the device
Current Time | 13 | Read Write | Time |  | Current UNIX time of the device. The LWM2M Client should be responsible to increase this time value as every second elapses.
Memory Free | 10 | Read | Integer | KB | Estimated current available memory of storage space which can store data and software in device
Memory Total | 21 | Read | Integer | KB | Total amount of storage space which can store data and software in the device
Battery Level | 9 | Read | Integer | 0-100% | Current battery level. Range: 0-100
Battery Status | 20 | Read | Integer | 0-6 | Battery Status. Range 0-6 (Normal, Charging, Charge Complete, Damage, Low Battery, Not Installed, Unknown)

## Slide 21: Current supported resources in Firmware Update Object
Resource Name | Resource ID | Operation | Type | Range and Units | Description
Package | 0 | Write | Opaque |  | Firmware package
Package URI | 1 | Write | String | 0-255 bytes | URI from where the device can download the firmware package by an alternative mechanism.
Update | 2 | Execute |  |  | Updates Firmware by using the firmware package stored in Package, or, by using the firmware downloaded from the package URI.
State | 3 | Read | Integer | 1-3 | State of firmware update (Idle, Downloading, Downloaded)
Update Result | 5 | Read | Integer | 0-6 | Contains the results of downloading or updating firmware
PkgName | 6 | Read | String | 0-255 bytes | Name of Firmware Package
PackageVersion | 7 | Read | String | 0-255 bytes | Version of Firmware Package

## Slide 22: Current supported resources in Server Object
Resource Name | Resource ID | Operation | Type | Range and Units | Description
Default Minimum Period | 2 | Read Write | Integer | Seconds | Default value device should use for the minimum Period of Observation in the absence of this parameter being included in an observation
Default Maximum Period | 3 | Read Write | Integer | Seconds | Default value device should use for the maximum Period of Observation in the absence of this parameter being included in an observation
Lifetime | 1 | Read Write | Integer |  | Specify the lifetime of the registration in seconds

## Slide 23: Mechanisms to control Observation
Observable Parameter | Description | Supported in Private Preview
Start | Start an observation | Yes
Stop | Stop an observation | No
P min | Minimum observation quiet period, to limit notification frequency | No
P max | Maximum observation quiet period, to guarantee notifications | No
Less than | Low limit measurement notification, like low alarm | No
Greater than | High limit measurement notification, like a high alarm | No
Step | Minimum delta change required to notify | No